## Slide 1
GridSense
AIoT Energy, Equipment & Worker Safety Monitoring
Hackathon Solution • PS-02
“Monitor the machine. Protect the worker. Act before failure.”

## Slide 2
01 • Problem & Objective
GridSense problem statement translated into a practical IoT solution
The Problem
Factories, workshops and buildings operate many electrical loads.
Equipment-level monitoring is often limited or disconnected.
Rising current, temperature, vibration or power can indicate abnormal operation.
Failures may be noticed only after energy loss, downtime or safety risk.
Our Objective
Continuously measure electrical and equipment parameters.
Identify abnormal operating conditions in real time.
Show energy consumption and equipment health on one dashboard.
Use a Smart Band to warn nearby workers when a hazardous condition is detected.
How much energy is each load consuming, is it operating normally, and when should action be taken?
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 2

## Slide 3
02 • Proposed Solution
One platform connecting equipment telemetry, AI-based anomaly detection and a worker Smart Band
EQUIPMENT
Sensors + ESP32
INTELLIGENCE
Rules + AI anomaly logic
SAFETY
Smart Band alerts
Equipment Monitoring
Voltage, current, power and energy consumption
Temperature and vibration
Load status, runtime and overload detection
Worker Safety Layer
BLE-linked wearable Smart Band
Haptic/visual warning when abnormal equipment is nearby
Emergency/SOS button and fall/impact detection
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 3

## Slide 4
03 • System Architecture
Real-time sensing → connectivity → intelligence → action
ELECTRICAL LOAD
Motor / Pump / HVAC
SENSORS
Current • Voltage Temp • Vibration
EDGE DEVICE
ESP32 / Gateway
CLOUD / API
MQTT • Database
DASHBOARD
Live UI
AI / Rule Engine
Thresholds + trend analysis
Anomaly score and risk level
Alert Engine
Dashboard notification
Smart Band vibration / warning
Action
Inspect equipment
Optional relay/load control
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 4

## Slide 5
04 • GridSense Smart Band
A wearable safety extension for workers near monitored equipment
⚠ ALERT
MOTOR ABNORMAL
MOVE TO SAFE AREA
Wearable Functions
BLE communication with gateway
Vibration/haptic warning
Emergency SOS button
Accelerometer for fall/impact detection
Optional location and environmental sensing
Smart Safety Logic
Equipment abnormality detected
Worker is inside a defined safety zone
Risk level increases
Band vibrates and dashboard raises alert
Supervisor can initiate inspection
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 5

## Slide 6
05 • Live Demo Scenario
A simple representative setup can demonstrate the complete value chain
1
Normal
Motor consumes normal power
2
Change
Load increases; current rises
3
Detect
Temp/vibration trend becomes abnormal
4
Protect
Nearby worker receives Smart Band alert
5
Act
Dashboard recommends inspection
Demo outcome: real-time monitoring + early warning + worker protection + actionable response
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 6

## Slide 7
06 • Dashboard & Analytics
A single control layer for energy, equipment health and safety events
TOTAL POWER
12.8 kW
ENERGY TODAY
86.4 kWh
ACTIVE LOADS
07
ALERTS
02
Power consumption trend
Live Alerts
⚠ Motor-02: abnormal vibration
⚠ Load-05: overload trend
Band alert: worker nearby
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 7

## Slide 8
07 • Technology Stack & Implementation
Prototype-first architecture designed for a reliable hackathon demo
Hardware
ESP32 / ESP32-S3
Current & voltage sensing
Temperature sensor
Vibration / accelerometer sensor
Relay module for optional control
Smart Band prototype
Software
MQTT / HTTP telemetry
Backend API + database
Real-time dashboard
Rule-based anomaly detection
Historical analytics
Notification service
AI / Future Scale
Anomaly scoring
Trend-based prediction
Equipment health score
Energy optimization insights
Multiple equipment support
Role-based supervisor view
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 8

## Slide 9
08 • Expected Impact
Designed around the outcomes requested by the GridSense challenge
ENERGY VISIBILITY
Know how much each load consumes.
EARLY DETECTION
Spot abnormal current, power, heat and vibration.
WORKER SAFETY
Warn workers through the Smart Band.
ACTIONABLE ALERTS
Turn sensor data into clear next steps.
HISTORICAL INSIGHTS
Compare trends and identify recurring problems.
SCALABLE PLATFORM
Extend from one demo load to many facilities.
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 9

## Slide 10
GridSense — From Data to Action
A unified AIoT layer for energy efficiency, equipment reliability and worker safety
SENSE → UNDERSTAND → ALERT → ACT
Equipment health + energy intelligence + Smart Band safety
Thank You • Questions?
GridSense • AIoT Energy, Equipment & Worker Safety Monitoring 10